## Slide 1: NTC Temporal Monitor Run Fault Overview - NTC 0x041
FDD: ES005A
Description:
This diagnostic is responsible for detecting Temporal Monitor Run Time faults.
Diagnostic Overview:
The temporal Monitor Function monitors the POE output of the Temporal Monitor IC (A4412) and if the POE is low, A SPI message is sent to the IC to check the type of Fault (WatchDog Fault or Non-WatchDog Fault). This Fault is captured by NTC 0x041.
Typical Fault Response:
  F3 Failure
Probable Sources (Most to Least Probable):
    Temporal Monitor IC(A4412) fault.
    WD_Monitor pulse fault.
    POE fault.
Rev: 1.0
Modified: nn-Jan-13
Initialization | 
Periodic | X
Event | 
Bit | Cause
0 | WatchDog type Failure
1 | Non-WatchDog type Failure.
2 | Unused
3 | Unused
4 | Unused
5 | Unused
6 | Unused
7 | Unused

## Slide 2: Revision Log
Rev | Revision
 | Initial Release