## Slide 1: NTC Temporal Monitor Init Fault Overview - NTC 0x040
FDD: ES005A
Description:
This diagnostic is responsible for detecting Temporal Monitor Initialization faults.
Diagnostic Overview:
The temporal Monitor initialization has a sequence of events. Faults at any one of these events are captured by the NTC 0x040. The sequence of events are monitored by a counter variable TmplMonrInitCntr.
Typical Fault Response:
  F1 Failure
Probable Sources (Most to Least Probable):
    Temporal Monitor IC(A4412) fault.
    Temporal Monitor SPI fault.
    WD_Monitor pulse fault.
    POE fault.
Rev: 1.0
Modified: nn-Jan-13
Initialization | 
Periodic | X
Event | 
Bit | Cause
0 | Fault Occured Between TmplMonrInitCntr = 10 ~ 11
1 | Fault Occured Between TmplMonrInitCntr = 13(AND Gate Fault)
2 | Fault Occured Between TmplMonrInitCntr = 15 ~ 16
3 | Fault Occured at TmplMonrInitCntr = 18 (POE Fault)
4 | Fault Occured at TmplMonrInitCntr = 19 (WD_STATE Fault)
5 | Fault Occured at TmplMonrInitCntr = 21 (Edge/Valid Write Fault)
6 | Fault Occured at TmplMonrInitCntr = 53 (POE + Non-WD Fault)
7 | Fault Occured at TmplMonrInitCntr = 53 (POE + WD Fault)

## Slide 2: Revision Log
Rev | Revision
 | Initial Release