## Slide 1: NTC Overview NTC 0x0A2.0 High Friction NTC (Reduced Performance)
Description:
This diagnostic logs a fault when the system friction value exceeds a calibrated threshold
Diagnostic Overview:
Friction learning is very important function which helps us compensate for current friction through Hystersis compensation
When the estimated friction is above a specified threshold, a diagnostic flag is set to warn the driver of high friction within the system
Typical Fault Response:
Response for this diagnostic is F3
The fault is latched with ignition cycle
Probable Sources (Most to Least Probable):
Environment conditions causing rust formation and enhancing internal friction of the system
High friction due to unwanted accumulation of materials/debris
Rev: 1.0
Modified: 22MY13
Initialization | 
Periodic | X
Event | 

## Slide 2: Algorithm Changes / Lessons Learned / Revision Log
Date | Revision | Initials
08FE16 | Initial Release | JK
Description of Unusual Event setting NTC | Root Cause / Explanation
Date | FDD & Rev | Modifications to Diagnostic Function