## Slide 1: NTC Overview NTC 0x0A4.(0-2) Absolute Temperature Thermal Limit
Description:
This diagnostic logs a fault when either the controller temperature or copper temperature estimate exceed calibrated values.
Diagnostic Overview:
The system components are designed to operated below specific temperature thresholds. If these threshold values are exceeded, a limit is applied to the system via limit tables to protect the components, and a diagnostic flag is set.
This is a recoverable fault that clears once the controller temperature or copper temperature fall below the calibrated thresholds.
Typical Fault Response:
Response for this diagnostic is F3.
This fault is recoverable once the temperature values fall below the threshold within an ignition cycle.
Probable Sources (Most to Least Probable):
Excessive system usage
System is exposed to high ambient temperature.
Rev: 1.0
Modified: 22MY13
Initialization | 
Periodic | X
Event | 
Bit | Cause
0 | Limiting due to Controller Temperature
1 | Limiting due to Copper Temperature
2 | Limiting due to Both Temperatures

## Slide 2: Algorithm Changes / Lessons Learned / Revision Log
Date | Revision | Initials
08FE16 | Initial Release | JK
10Au16 | Update the bits table with 3 bits used in the NTC | PP
Description of Unusual Event setting NTC | Root Cause / Explanation
Date | FDD & Rev | Modifications to Diagnostic Function