## Slide 1: NTC Overview NTC 0x0E1.0
Description:
When Software Rack Limiter (SRL) is enabled, SF011A receives Handwheel Angle End of
travel Clockwise and Counter Clockwise signals (Signal 0 and Signal 1) and its availability
status from CM650 and CM660.
The NTC will be set in SF011A when Cw and Ccw Eot signals are not available or if signals do
not correlate or if signals are out of range.
Diagnostic Overview:
The NTC 0x0E1 will be set when any one of the following conditions occur:
When Eot Cw and Ccw signals (Signal 0 an Signal 1) are not available for 500 msec, Signal Available Fault ( Bit 0 of NTC 0X0E1) is set and NTC is set to “FAILED”.
When Eot Cw and Ccw signals are available but either of Cw or Ccw signals do not correlate each other then Correlation Fault ( Bit 1 of NTC 0X0E1) is set and NTC is set to “FAILED” instantaneously.
When Eot Cw and Ccw signals are available but either of Cw or Ccw Eot signal is out of range then Out of Range Fault ( Bit 2 of NTC 0x0E1) is set and NTC is set to “FAILED” instantaneously.
NTC 0x0E1 is set to PASS when Cw and Ccw Eot are both available, within range and correlate each other.
Typical Fault Response:
- Response for this diagnostic is F3
Probable Sources (Most to Least Probable):
    Wrong C-factor cal set
    Connection to control module (no connection)
    Sensor fault
    Control module interface circuit failure
Rev: 1.0
Modified: nn-Jan-13
Initialization | 
Periodic | X
Event | 

## Slide 2: Algorithm Changes / Lessons Learned / Revision Log
Date | Revision | Initials
18may2016 | Initial Release | Sudeep Shankar
Description of Unusual Event setting NTC | Root Cause / Explanation
Date | FDD & Rev | Modifications to Diagnostic Function
18May2016 | SF011A 2.0.0 | Initial version