## Slide 1: EOT Damping Command Boundary Reached Overview NTC 0x0C6.0
SF018A EOT Protection
FDD: SF027A
Description:
A diagnostic fault is triggered when the EOT Damping command reaches or exceeds the
firewall safety boundary.
Diagnostic Overview:
The EOT Protection Firewall applies a limiting boundary on the EOT Damping Command. The NTC is only triggered to provide notification of that limiting has occurred during the current controller power cycle. The safety limit value is conditionally applied based upon steering wheel angle and vehicle speed. There is no debounce time allocated for the NTC (eg pass step, fail step).
Typical Fault Response:
  LOA Based Systems
    F3
  Non-LOA Based Systems
    F3
Probable Sources (Most to Least Probable):
  Systematic fault within the primary return command function
  Corrupted calibration of the EOTDamping firewall safety boundary
Rev: 1.0
Modified: nn-Jan-13
Initialization | 
Periodic | X
Event | 
SF027A EOT Protection Firewall
Steering
Signals
Safety Boundary
EOT Damping Calculation
Limit
NTC 0x0C6.0
EotDampgCmd
EotDampgCmdLimd
Steering
Position
& Vehicle Speed

## Slide 2: EOT Active Command Boundary Reached Overview NTC 0x0C6.1
SF018A EOT Protection
FDD: SF027A
Description:
A diagnostic fault is triggered when the EOT Active command reaches or exceeds the
firewall safety boundary.
Diagnostic Overview:
The EOT Protection Firewall applies a limiting boundary on the EOT Active Command (eg software rack limiter command). The NTC is only triggered to provide notification of that limiting has occurred during the current controller power cycle. The safety limit value is conditionally applied based upon steering wheel angle and vehicle speed. There is no debounce time allocated for the NTC (eg pass step, fail step).
Typical Fault Response:
  LOA Based Systems
    F3
  Non-LOA Based Systems
    F3
Probable Sources (Most to Least Probable):
  Systematic fault within the primary return command function
  Corrupted calibration of the EOT Active firewall safety boundary
Rev: 1.0
Modified: nn-Jan-13
Initialization | 
Periodic | X
Event | 
SF027A EOT Protection Firewall
Steering
Signals
Safety Boundary
EOT Active Calculation
Limit
NTC 0x0C6.1
EotActvCmd
EotActvCmdLimd
Steering
Position & Vehicle Speed

## Slide 3: Revision Log
Rev | Revision
1.0 | Initial Release